奖励函数部分
(1)机体目标高度
_reward_base_height
self.cfg.rewards.base_height_target

(2)关节极限
self.dof_pos_limits soft_dof_vel_limit soft_torque_limit

(3)脚在空中的时间
min_feet_air_time，max_feet_air_time

（4）脚的最大接触力
max_contact_force

（5）
min_feet_distance

beifne
from legged_gym.envs.base.base_config import BaseConfig

class TITAPointFootRoughCfg(BaseConfig):
class env:
num_envs = 4096
num_propriceptive_obs = 27
num_privileged_obs = 148 # if not None a priviledge_obs_buf will be returned by step() (critic obs for assymetric training). None is returned otherwise
num_actions = 6
env_spacing = 3.0 # not used with heightfields/trimeshes
send_timeouts = True # send time out information to the algorithm
episode_length_s = 20 # episode length in seconds

class terrain:
mesh_type = "trimesh" # "heightfield" # none, plane, heightfield or trimesh
horizontal_scale = 0.1 # [m]
vertical_scale = 0.005 # [m]
border_size = 25 # [m]
curriculum = True
static_friction = 0.4
dynamic_friction = 0.6
restitution = 0.8
# rough terrain only:
measure_heights_actor = False
measure_heights_critic = True
measured_points_x = [
-0.5,
-0.4,
-0.3,
-0.2,
-0.1,
0.0,
0.1,
0.2,
0.3,
0.4,
0.5,
] # 1mx1m rectangle (without center line)
measured_points_y = [-0.5, -0.4, -0.3, -0.2, -0.1, 0.0, 0.1, 0.2, 0.3, 0.4, 0.5]
selected = False # select a unique terrain type and pass all arguments
terrain_kwargs = None # Dict of arguments for selected terrain
max_init_terrain_level = 5 # starting curriculum state
terrain_length = 8.0
terrain_width = 8.0
num_rows = 10 # number of terrain rows (levels)
num_cols = 20 # number of terrain cols (types)
# terrain types: [smooth slope, rough slope, stairs up, stairs down, discrete]
terrain_proportions = [0.1, 0.1, 0.35, 0.25, 0.2]
# trimesh only:
slope_treshold = (
0.75 # slopes above this threshold will be corrected to vertical surfaces
)

class commands:
curriculum = False
max_curriculum = 1.0
num_commands = 4 # default: lin_vel_x, lin_vel_y, ang_vel_yaw, heading (in heading mode ang_vel_yaw is recomputed from heading error)
resampling_time = 10.0 # time before command are changed[s]
heading_command = True # if true: compute ang vel command from heading error

class ranges:
lin_vel_x = [-1.0, 1.0] # min max [m/s]
lin_vel_y = [-0.2, 0.2] # min max [m/s]
ang_vel_yaw = [-1, 1] # min max [rad/s]
heading = [-3.14, 3.14]
# lin_vel_x = [0.3, 0.5] # min max [m/s]
# lin_vel_y = [0, 0] # min max [m/s]
# ang_vel_yaw = [0, 0] # min max [rad/s]
# heading = [0, 0]

class init_state:
pos = [0.0, 0.0, 0.4] # x,y,z [m]
rot = [0.0, 0.0, 0.0, 1.0] # x,y,z,w [quat]
lin_vel = [0.0, 0.0, 0.0] # x,y,z [m/s]
ang_vel = [0.0, 0.0, 0.0] # x,y,z [rad/s]
default_joint_angles = { # target angles when action = 0.0
"joint_left_leg_1": -0.27,
"joint_right_leg_1": 0.27,
"joint_left_leg_2": 0.28,
"joint_right_leg_2": 0.28,
"joint_left_leg_3": -0.73,
"joint_right_leg_3": -0.73,
"joint_left_leg_4": 0,
"joint_right_leg_4": 0,
# "joint_left_leg_1": 0.24,
# "joint_left_leg_2": 1.6,
# "joint_left_leg_3": -2.67,
# "joint_right_leg_1": -0.28,
# "joint_right_leg_2": 1.6,
# "joint_right_leg_3": -2.67,
}

class control:
control_type = "P" # P: position, V: velocity, T: torques
# PD Drive parameters:
stiffness = {
"joint_left_leg_1": 80,
"joint_right_leg_1": 80,
"joint_left_leg_2": 80,
"joint_right_leg_2": 80,
"joint_left_leg_3": 80,
"joint_right_leg_3": 80,
} # [N*m/rad]
damping = {
"joint_left_leg_1": 1.5,
"joint_right_leg_1": 1.5,
"joint_left_leg_2": 1.5,
"joint_right_leg_2": 1.5,
"joint_left_leg_3": 1.5,
"joint_right_leg_3": 1.5,
} # [N*m*s/rad]
# action scale: target angle = actionScale * action + defaultAngle
action_scale = 0.1
# decimation: Number of control action updates @ sim DT per policy DT
decimation = 4

class asset:
import os
import sys

robot_type = os.getenv("ROBOT_TYPE")

# Check if the ROBOT_TYPE environment variable is set, otherwise exit with an error
if not robot_type:
print(
"Error: Please set the ROBOT_TYPE using 'export ROBOT_TYPE=<robot_type>'."
)
sys.exit(1)
file = (
"{LEGGED_GYM_ROOT_DIR}/resources/robots/tita_pointfoot/"
+ robot_type
+ "/urdf/tita_description.urdf"
)
name = robot_type
foot_name = "_leg_4"
terminate_after_contacts_on = ["base_link"]
penalize_contacts_on = ["base_link", "_leg_3"]
disable_gravity = False
collapse_fixed_joints = False # merge bodies connected by fixed joints. Specific fixed joints can be kept by adding " <... dont_collapse="true">
fix_base_link = False # fixe the base of the robot
default_dof_drive_mode = 3 # see GymDofDriveModeFlags (0 is none, 1 is pos tgt, 2 is vel tgt, 3 effort)
self_collisions = 0 # 1 to disable, 0 to enable...bitwise filter
replace_cylinder_with_capsule = True # replace collision cylinders with capsules, leads to faster/more stable simulation
flip_visual_attachments = (
False # Some .obj meshes must be flipped from y-up to z-up
)

density = 0.001
angular_damping = 0.0
linear_damping = 0.0
max_angular_velocity = 1000.0
max_linear_velocity = 1000.0
armature = 0.0
thickness = 0.01

class domain_rand:
randomize_friction = True
friction_range = [0.0, 1.6]
randomize_base_mass = True
added_mass_range = [-1.0, 2.0]
randomize_base_com = True
rand_com_vec = [0.03, 0.02, 0.03]
push_robots = True
push_interval_s = 7
max_push_vel_xy = 0.6

class rewards:
class scales:
action_rate = -0.01
ang_vel_xy = -0.5
base_height = -10.0
collision = -50.0
dof_acc = -2.5e-07
dof_pos_limits = -0.0
dof_vel = -0.0
feet_air_time = 60
feet_contact_forces = -0.01
feet_stumble = -0.0
lin_vel_z = -0.5
no_fly = 10.0
double_support = -1
orientation = -5.0
stand_still = -1.0
termination = -0.0
torque_limits = -0.01
torques = -2.5e-05
tracking_ang_vel = 5
tracking_lin_vel = 10.0
unbalance_feet_air_time = -300.0
unbalance_feet_height = -60.0
feet_distance = -100
survival = 100

base_height_target = 0.38
soft_dof_pos_limit = (
0.95 # percentage of urdf limits, values above this limit are penalized
)
soft_dof_vel_limit = 0.9
soft_torque_limit = 0.8
max_contact_force = 200.0 # forces above this value are penalized
only_positive_rewards = False # if true negative total rewards are clipped at zero (avoids early termination problems)
min_feet_distance = 0.05
min_feet_air_time = 0.25
max_feet_air_time = 0.65
tracking_sigma = 0.25 # tracking reward = exp(-error^2/sigma)

class normalization:
class obs_scales:
lin_vel = 2.0
ang_vel = 0.25
dof_pos = 1.0
dof_vel = 0.05
height_measurements = 5.0

clip_observations = 100.0
clip_actions = 100.0

class noise:
add_noise = True
noise_level = 1.0 # scales other values

class noise_scales:
dof_pos = 0.01
dof_vel = 1.5
lin_vel = 0.1
ang_vel = 0.2
gravity = 0.05
height_measurements = 0.1

# viewer camera:
class viewer:
ref_env = 0
pos = [10, 0, 6] # [m]
lookat = [11.0, 5, 3.0] # [m]

class sim:
dt = 0.005
substeps = 1
gravity = [0.0, 0.0, -9.81] # [m/s^2]
up_axis = 1 # 0 is y, 1 is z

class physx:
num_threads = 10
solver_type = 1 # 0: pgs, 1: tgs
num_position_iterations = 4
num_velocity_iterations = 0
contact_offset = 0.01 # [m]
rest_offset = 0.0 # [m]
bounce_threshold_velocity = 0.5 # 0.5 [m/s]
max_depenetration_velocity = 1.0
max_gpu_contact_pairs = 2**23 # 2**24 -> needed for 8000 envs and more
default_buffer_size_multiplier = 5
contact_collection = (
2 # 0: never, 1: last sub-step, 2: all sub-steps (default=2)
)

class TITAPointFootRoughCfgPPO(BaseConfig):
seed = 1
runner_class_name = "OnPolicyRunner"

class policy:
init_noise_std = 1.0
actor_hidden_dims = [512, 256, 128]
critic_hidden_dims = [512, 256, 128]
activation = "elu" # can be elu, relu, selu, crelu, lrelu, tanh, sigmoid
# only for 'ActorCriticRecurrent':
# rnn_type = 'lstm'
# rnn_hidden_size = 512
# rnn_num_layers = 1

class algorithm:
# training params
value_loss_coef = 1.0
use_clipped_value_loss = True
clip_param = 0.2
entropy_coef = 0.01
num_learning_epochs = 5
num_mini_batches = 4 # mini batch size = num_envs*nsteps / nminibatches
learning_rate = 1.0e-3 # 5.e-4
schedule = "adaptive" # could be adaptive, fixed
gamma = 0.99
lam = 0.95
desired_kl = 0.01
max_grad_norm = 1.0

class runner:
policy_class_name = "ActorCritic"
algorithm_class_name = "PPO"
num_steps_per_env = 24 # per iteration
max_iterations = 100000 # number of policy updates

# logging
save_interval = 200 # check for potential saves every this many iterations
experiment_name = "tita_pointfoot_rough"
run_name = ""
# load and resume
resume = False
load_run = -1 # -1 = last run
checkpoint = -1 # -1 = last saved model
resume_path = None # updated from load_run and chkpt